## Slide 1: BOOLEAN ALGEBRA
BY:
ROSHNI PATOA
COMPUTER SYSTEM ARCHITECTURE

## Slide 2: INTRODUCTION
Boolean algebra is the set of rules used to simplify the given logic expression without changing its functionality.
It is used when the number of variables are less.
It is a form of algebra that deals with single digit binary values and variables.
Values and variables can indicate some of the following binary pairs of values:
    ON/OFF
    TRUE/FALSE
    HIGH/LOW
    CLOSED/OPEN
    1/0

## Slide 3: APPLICATIONS OF BOOLEAN ALGEBRA:
It is used to perform the logical operations in digital computer.
Logical operations are performed by logical operators. The fundamental logical operators are:
1. AND (conjunction)
2. OR (disjunction)
3. NOT (negation/complement)

## Slide 4: AND OPERATOR
It performs logical multiplication and denoted by (.) dot.
X | Y | X.Y
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 5
OR OPERATOR
It performs logical addition and denoted by (+) dot.
X | Y | X+Y
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1

## Slide 6
NOT OPERATOR
It performs logical negation and denoted by (-) bar. It operates on single variable.
X | X´
0 | 1
1 | 0

## Slide 7: TRUTH TABLE
Truth table is a table that contains all possible values of logical variables/statements in a Boolean expression.
No. of possible combination =
2n, where n=number of variables used in a Boolean expression.

## Slide 8
BASIC PROPERTIES OF BOOLEAN ALGEBRA
T1 : Properties of 0
  (a) 0 + A = A (b) 0 . A = 0
T2 : Properties of 1
  (a) 1 + A = 1 (b) 1 . A = A

## Slide 9
BASIC PROPERTIES OF BOOLEAN ALGEBRA
T3 : Commutative Law
  (a) A + B = B + A (b) A . B = B . A
T4 : Associate Law
  (a) (A + B) + C = A + (B + C) (b) (A . B). C = A .(B . C)
T5 : Distributive Law
  (a) A .(B + C) = A. B + A. C (b) A + (B. C) = (A + B) .(A + C)
  (c) A+A’B = A+B

## Slide 10
BASIC PROPERTIES OF BOOLEAN ALGEBRA
T6 : Indempotence (Identity ) Law
  (a) A + A = A (b) A .A = A
T7 : Absorption (Redundance) Law
  (a) A + A .B = A (b) A (A + B) = A

## Slide 11
BASIC PROPERTIES OF BOOLEAN ALGEBRA
T8 : Complementary Law
  (a) X+X’=1
  (b) X.X’=0
T9 : Involution
  (a) x’’ = x
T10 : De-Morgan's Theorem
  (a) (X.Y)’=X’+Y’
  (b) (X+Y)’=X’.Y’

## Slide 12
REDUCE USING BOOLEAN ALGEBRA
F = B.A.C’ + B’.A.C’ + B.C’
F = A.B + A.B’
F = A.B + A.B’.C + A.B’.C’
F = (A+B+C).(A+B’+C).(A+B+C’)
F = (A+B).(A+B’).(A’+B).(A’+B’)