## Slide 1: COMBINATIONAL CIRCUITS
BY:
ROSHNI PATOA
COMPUTER SYSTEM ARCHITECTURE

## Slide 2: ENCODER
The combinational circuits that change the binary information into N output lines are known as Encoders. The binary information is passed in the form of 2N input lines. The output lines define the N-bit code for the binary information. In simple words, the Encoder performs the reverse operation of the Decoder. At a time, only one input line is activated for simplicity. The produced N-bit output code is equivalent to the binary information.

## Slide 3: 4X2 Encoder
In 4X2 encoder, there are total of four inputs, i.e., Y0, Y1, Y2, and Y3, and two outputs, i.e., A0 and A1. In 4-input lines, one input-line is set to true at a time to get the respective binary code in the output side. Below are the block diagram and the truth table of the 4 to 2 line encoder.

## Slide 4: Truth Table for 4X2 Encoder
The logical expression of the term A0 and A1 is as follows:
A1=Y3+Y2 A0=Y3+Y1

## Slide 5
LOGIC DIAGRAM for 4X2 Encoder

## Slide 6: 8x3 ENCODER
The 8x3 Encoder is also known as Octal to Binary Encoder. In 8x3 encoder, there is a total of eight inputs, i.e., Y0, Y1, Y2, Y3, Y4, Y5, Y6, and Y7 and three outputs, i.e., A0, A1, and A2. In 8-input lines, one input-line is set to true at a time to get the respective binary code in the output side. Below are the block diagram and the truth table of the 8x3 encoder.

## Slide 7: Truth Table for 8x3 ENCODER
The logical expression of the term A0, A1, and A2 are as follows:
A2=Y4+Y5+Y6+Y7 A1=Y2+Y3+Y6+Y7 A0=Y7+Y5+Y3+Y1

## Slide 8
LOGIC DIAGRAM for 8x3 ENCODER