## Slide 1: COMBINATIONAL CIRCUITS
BY:
ROSHNI PATOA
COMPUTER SYSTEM ARCHITECTURE

## Slide 2: HALF ADDER
A half adder is a basic digital circuit
It performs addition of two binary digits
Has two inputs (A and B) and two outputs (Sum and Carry)
Key component in arithmetic operations in computers

## Slide 3: Inputs and Outputs
Inputs: Two 1-bit binary numbers (A and B)
Outputs:
    Sum (S): Result of A + B
    Carry (C): Overflow bit when A + B > 1

## Slide 4: Truth Table for Half Adder

## Slide 5: Logic Gates in Half Adder
XOR gate: Used for Sum output
AND gate: Used for Carry output

## Slide 6
XOR GATE FOR SUM
XOR (Exclusive OR) gate used for Sum
Output is 1 if inputs are different
Output is 0 if inputs are same
Perfectly represents addition without carry

## Slide 7
AND GATE FOR CARRY
AND gate used for Carry
Output is 1 only when both inputs are 1
Represents when addition results in a carry

## Slide 8
Half Adder Circuit Diagram
Inputs: A and B
XOR gate connected to both inputs, output is Sum
AND gate connected to both inputs, output is Carry

## Slide 9
Example: Adding 0 + 0
Input A = 0, Input B = 0
XOR gate: 0 ⊕ 0 = 0 (Sum)
AND gate: 0 • 0 = 0 (Carry)
Result: Sum = 0, Carry = 0

## Slide 10
Example: Adding 0 + 1
Input A = 0, Input B = 1
XOR gate: 0 ⊕ 1 = 1 (Sum)
AND gate: 0 • 1 = 0 (Carry)
Result: Sum = 1, Carry = 0

## Slide 11
Example: Adding 1 + 0
Input A = 1, Input B = 0
XOR gate: 1 ⊕ 0 = 0 (Sum)
AND gate: 1 • 0 = 0 (Carry)
Result: Sum = 1, Carry = 0

## Slide 12
Example: Adding 1 + 1
Input A = 1, Input B = 1
XOR gate: 1 ⊕ 1 = 0 (Sum)
AND gate: 1 • 1 = 1 (Carry)
Result: Sum = 0, Carry = 1

## Slide 13
CONCLUSION
Half adders are fundamental to digital arithmetic
They combine XOR and AND gates for binary addition
Next steps: Explore full adders