## Slide 1: BCA Ist Semester Introduction of Logic Circuit and Digital Design(ILCDD) Course Code: BCAC0003
Presented by:
Mr.Anuj Kumar
Assistant Professor, Dept. Of CEA
GLA University, Mathura

## Slide 2: Karnaugh Maps
Karnaugh maps (K-maps) are graphical representations of boolean functions.
One map cell corresponds to a row in the truth table.
Also, one map cell corresponds to a minterm or a maxterm in the boolean expression
Multiple-cell areas of the map correspond to standard terms.

## Slide 3: Two-Variable Map
m3
m2
1
m1
m0
0
1
0
x1
x2
0
1
2
3
NOTE: ordering of variables is IMPORTANT for f(x1,x2), x1 is the row, x2 is the column.
Cell 0 represents x1’x2’; Cell 1 represents x1’x2; etc. If a minterm is present in the function, then a 1 is placed in the corresponding cell.
m3
m1
1
m2
m0
0
1
0
x2
x1
0
2
1
3
OR

## Slide 4: 2-Variable Map -- Example
f(x1,x2) = x1’x2’+ x1’x2 + x1x2’ = m0 + m1 + m2 = x1’ + x2’
1s placed in K-map for specified minterms m0, m1, m2
Grouping (ORing) of 1s allows simplification
What (simpler) function is represented by each dashed rectangle?
  x1’ = m0 + m1
  x2’ = m0 + m2
Note m0 covered twice
x1 | 0 | 1
0 | 1 | 1
1 | 1 | 0
x2
0
1
2
3

## Slide 5: Minimization as SOP using K-map
Enter 1s in the K-map for each product term in the function
Group adjacent K-map cells containing 1s to obtain a product with fewer variables. Group size must be in power of 2 (2, 4, 8, …)
Handle “boundary wrap” for K-maps of 3 or more variables.
Realize that answer may not be unique

## Slide 6: Three-Variable Map
m6
m7
m5
m4
1
m2
m3
m1
m0
0
10
11
01
00
yz
x
0
1
3
2
4
5
7
6
-Note: variable ordering is (x,y,z); yz specifies column, x specifies row.
-Each cell is adjacent to three other cells (left or right or top or bottom or edge wrap)

## Slide 7: Three-Variable Map (cont.)
The types of structures that are either minterms or are generated by repeated application of the minimization theorem on a three variable map are shown at right. Groups of 1, 2, 4, 8 are possible.
minterm
group of 2 terms
group of 4 terms

## Slide 8: Simplification
Enter minterms of the Boolean function into the map, then group terms
Example: f(a,b,c) = a’c + abc + bc’
Result: f(a,b,c) = a’c+ b
 | 1 | 1 | 1
 |  | 1 | 1
a
bc
 | 1 | 1 | 1
 |  | 1 | 1

## Slide 9: More Examples
f1(x, y, z) = ∑ m(2,3,5,7)
f2(x, y, z) = ∑ m (0,1,2,3,6)
f1(x, y, z) = x’y + xz
f2(x, y, z) = x’+yz’
yz X | 00 | 01 | 11 | 10
0 |  |  | 1 | 1
1 |  | 1 | 1 | 
1 | 1 | 1 | 1
 |  |  | 1

## Slide 10: Four-Variable Maps
Top cells are adjacent to bottom cells. Left-edge cells are adjacent to right-edge cells.
Note variable ordering (WXYZ).
m10
m11
m9
m8
10
m14
m15
m13
m12
11
m6
m7
m5
m4
01
m2
m3
m1
m0
00
10
11
01
00
WX
YZ

## Slide 11: Four-variable Map Simplification
One square represents a minterm of 4 literals.
A rectangle of 2 adjacent squares represents a product term of 3 literals.
A rectangle of 4 squares represents a product term of 2 literals.
A rectangle of 8 squares represents a product term of 1 literal.
A rectangle of 16 squares produces a function that is equal to logic 1.

## Slide 12: Example
Simplify the following Boolean function (A,B,C,D) = ∑m(0,1,2,4,5,7,8,9,10,12,13).
First put the function g( ) into the map, and then group as many 1s as possible.
cd
ab
1
1
1
1
1
1
1
1
1
1
1
g(A,B,C,D) = c’+b’d’+a’bd
1
1
1
1
1
1
1
1
1
1
1