## Slide 1: BCA Ist Semester Introduction of Logic Circuit and Digital Design(ILCDD) Course Code: BCAC003
Presented by:
Mr.Anuj Kumar
Assistant Professor, Dept. Of CE&A
GLA University, Mathura

## Slide 2: Encoder/Decoder
ENCODER- a digital circuit that produces a binary output code depending on which of its inputs are activated.
DECODER- a digital circuit that converts an input binary code into a single numeric output.
A0 A1 A2 A3 A4 A5 A6 A7
ENCODER
O0 O1 O2
A0 A1 A2
O0 O1 O2 O3 O4 O5 O6 O7
DECODER

## Slide 3: Encoders
Binary code of N digits can be used to store 2N distinct elements of coded information.
Encoders convert 2N lines of input into a code of N
bits and

## Slide 4: Encoder Example
Example: 4-to-2 binary encoder
In encoder circuit only one input may be set high (1) at a
certain time.
The output is a 2-bit number.
I3 | I2 | I1 | I0 | Y1 | Y0
0 | 0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 0 | 0 | 1
0 | 1 | 0 | 0 | 1 | 0
1 | 0 | 0 | 0 | 1 | 1
I0
I
1
I2
I3
Y1
Y0

## Slide 5: Encoder Example
Example: 8-to-3 binary encoder (octal-to-binary)
A0 | = | D1 | + | D3 | + | D5 | + | D7
A1 | = | D2 | + | D3 | + | D6 | + | D7
A2 | = | D4 | + | D5 | + | D6 | + | D7

## Slide 6: Encoder Example (cont.)

## Slide 8: Decoders

## Slide 9: Binary Decoders
Binary decoders convert an n-bit input to a single output. It uses its n-bit input to determine which of the 2n outputs will be uniquely activated.
The outputs of a decoder are minterms. That is why decoders are sometimes called as minterm generators.
We can easily use a decoder to implement any sum of minterms expression.
Note: A minterm is a Boolean expression resulting in 1 only for the output of a single row (in a truth table) or a single cell (in a Karnaugh map), and 0s for all other row or cells, respectively.

## Slide 10: 2-to-4 Binary Decoder
A circuit of 2-to-4 binary decoder is shown below.
Binary Decoder
2 inputs
4 outputs
Enable
The truth table shows that for any given input combination,
exactly one output will turn to 1.
The enable must be set to 1 to get an output.

## Slide 11: 3-to-8 Binary Decoder
0
1
2
3
4
5
6
X | Y | Z | F | F | F | F | F | F | F | F7
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
Try to understand the logic circuit of 3-to-8 binary decoder below.
Binary Decoder
3 inputs
8 outputs
Enable

## Slide 12
Combinational Circuit Design with Decoders
Example Realize F (X,Y,Z) = Σ (1, 4, 7) with a decoder:

## Slide 13: Decoder as a Logic Building Block

## Slide 14: Decoder as a Logic Building Block