## Slide 1: BCA Ist Semester Introduction of Logic Circuit and Digital Design(ILCDD) Course Code: BCAC0003
Presented by:
Mr.Anuj Kumar
Assistant Professor, Dept. Of CE&A
GLA University, Mathura

## Slide 2: Number Base Conversions
Decimal
(Base 10)
Octal
(Base 8)
Binary
(Base 2)
Hexadecimal
(Base 16)

## Slide 3: Decimal to other Base System
Step-1 Divide the decimal number to be converted by the value of the new Base.
Step-2 Get the remainder from Step 1 as the right most digit (LSB) of new base number.
Step-3 Divide the quotient of the previous divide by the new base.
Step-4 Record the remainder from Step 3 as the next digit (to the left) of new base.
Step-5 Repeat Step 3 and Step 4 until the quotient becomes Zero.

## Slide 4: Decimal to Binary Conversion
Divide the number by the ‘Base’ (=2)
Take the remainder (either 0 or 1) as a coefficient
Take the quotient and repeat the division
Example: (13)10
Quotient
Remainder
Coefficient
Answer: (13)10 = (a3 a2 a1 a0)2 = (1101)2
MSB LSB
13
/ 2 = 6
1 a0 = 1
6
/ 2 = 3
0 a1 = 0
3
/ 2 = 1
1 a2 = 1
1
/ 2 = 0
1 a3 = 1

## Slide 5: Decimal to Octal Conversion
Example: (264)10
Quotient
Remainder
Coefficient
Answer: (264)10 = (a2 a1 a0)8 = (410)8
264
/ 8 = 33
0 a0 = 0
33
/ 8 = 4
1 a1 = 1
4
/ 8 = 0
4 a2 = 4

## Slide 6: Decimal to Hexadecimal Conversion
Example: (10234)10
Quotient
Remainder
Coefficient
Answer: (10234)10 = (a3a2 a1 a0)16 = (27FA)16
10234
/ 16 = 639
10 a0 = 10=A
639
/ 16 = 39
15 a1 = 15=F
39
/ 16 = 2
7 a2 = 7
2
/ 16 = 0
2 a3 = 2

## Slide 7: Other Base to Decimal
Step-1 Determine the positional value of each digit depends on the position of the digit and the base of number system.
Step-2 Multiply the obtained column value by digits in corresponding columns.
Sum the product calculated.

## Slide 8: Binary to Decimal Conversion
Multiply the digit with 2(with place value exponent).
Eventually add all the multiplication becomes the Decimal number.

## Slide 9: Octal to Decimal Conversion
(345 )8 =(???)10
(3 * 82) + (4 * 81) + (5 * 80)
=(3 * 64) + (4 * 8) + (5 * 1)
= (229)10

## Slide 10: Hexadecimal to Decimal Conversion
(A14B)16 =(???)10
(A*163)+(1 * 162) + (4 * 161) + (B * 160)
=(4096*10)+(1 * 256) + (4 * 16) + (11 * 1)
= (41291)10

## Slide 11
THANK YOU