## Slide 1: BCA Ist Semester Introduction of Logic Circuit and Digital Design(ILCDD) Course Code: BCAC0003
Presented by:
Mr.Anuj Kumar
Assistant Professor, Dept. Of CE&A
GLA University, Mathura

## Slide 2: Decimal (Fraction) to Binary Conversion
Multiply the number by the ‘Base’ (=2)
Take the integer (either 0 or 1) as a coefficient
Take the resultant fraction and repeat the division
Example: (0.625)10
Integer
Fraction
Coefficient
Answer: (0.625)10 = (0.a-1 a-2 a-3)2 = (0.101)2
MSB LSB
0.625
* 2 = 1 . 25
0.25
* 2 = 0 . 5 a-2 = 0
0.5
* 2 = 1 . 0 a-3 = 1
a-1 = 1

## Slide 3: Decimal to Octal Conversion
Example: (175.3125)10
Quotient
Remainder
Coefficient
Answer: (175)10 = (a2 a1 a0)8 = (257)8
175
/ 8 = 21
7 a0 = 7
21
/ 8 = 2
5 a1 = 5
2
/ 8 = 0
2 a2 = 2
(0.3125)10
Integer
Fraction
Coefficient
Answer: (.3125)10 = (0.a-1 a-2 a-3)8 = (0.24)8
=(257.24)8
0.3125
* 8 = 2 . 5
0.5
* 8 = 4 . 0 a-2 = 4
a-1 = 2

## Slide 4: Decimal to Hexadecimal Conversion
Example: (2025.625)10
Quotient
Remainder
Coefficient
Answer: (175)10 = (a2 a1 a0)16 = (7E9)16
2025
/ 16 = 126
9 a0 = 9
126
/ 16 = 7
14 a1 = 14=E
7
/ 16 = 0
7 a2 = 7
Example: (0.625)10
Integer
Fraction
Coefficient
Answer: (0.625)10 = (0.a-1 a-2 a-3)8 = (0.A)16
=(7E9.A)16
0.625
* 16 = 10 . 0
a-1 = 10=A

## Slide 5: Binary − Octal Conversion
8 = 23
Each group of 3 bits represents an octal digit
Octal | Binary
0 | 0 0 0
1 | 0 0 1
2 | 0 1 0
3 | 0 1 1
4 | 1 0 0
5 | 1 0 1
6 | 1 1 0
7 | 1 1 1
Example:
( 1 0 1 1 0 . 0 1 )2
( 2 6 . 2 )8
Assume Zeros
Works both ways (Binary to Octal & Octal to Binary)

## Slide 6: Binary − Hexadecimal Conversion
16 = 24
Each group of 4 bits represents a hexadecimal digit
Hex | Binary
0 | 0 0 0 0
1 | 0 0 0 1
2 | 0 0 1 0
3 | 0 0 1 1
4 | 0 1 0 0
5 | 0 1 0 1
6 | 0 1 1 0
7 | 0 1 1 1
8 | 1 0 0 0
9 | 1 0 0 1
A | 1 0 1 0
B | 1 0 1 1
C | 1 1 0 0
D | 1 1 0 1
E | 1 1 1 0
F | 1 1 1 1
Example:
( 1 0 1 1 0 . 0 1 )2
( 1 6 . 4 )16
Assume Zeros
Works both ways (Binary to Hex & Hex to Binary)

## Slide 7: Octal − Hexadecimal Conversion
Convert to Binary as an intermediate step
Example:
( 0 1 0 1 1 0 . 0 1 0 )2
( 1 6 . 4 )16
Assume Zeros
Works both ways (Octal to Hex & Hex to Octal)
( 2 6 . 2 )8
Assume Zeros

## Slide 8: Decimal, Binary, Octal and Hexadecimal
Decimal | Binary | Octal | Hex
00 | 0000 | 00 | 0
01 | 0001 | 01 | 1
02 | 0010 | 02 | 2
03 | 0011 | 03 | 3
04 | 0100 | 04 | 4
05 | 0101 | 05 | 5
06 | 0110 | 06 | 6
07 | 0111 | 07 | 7
08 | 1000 | 10 | 8
09 | 1001 | 11 | 9
10 | 1010 | 12 | A
11 | 1011 | 13 | B
12 | 1100 | 14 | C
13 | 1101 | 15 | D
14 | 1110 | 16 | E
15 | 1111 | 17 | F

## Slide 9
THANK YOU