## Slide 1: BCA Ist Semester Introduction of Logic Circuit and Digital Design(ILCDD) Course Code: BCAC0003
Presented by:
Mr.Anuj Kumar
Assistant Professor, Dept. Of CE&A
GLA University, Mathura

## Slide 2: Arithmetic operations of Binary
Rules for Addition:-
0+0=0
0+1=1
1+0=1
1+1=0 (1 Carry)
101010 (42)
+ 110011 (51)
1011101 (93)

## Slide 3
Rules for Subtraction:-
0-0=0
0-1=1 with a borrow 1
1-0=1
1-1=0
1110 14
1011 11
0011 3

## Slide 4
Rules for Multiplication:-
0*0=0
0*1=0
1*0=0
1*1=1
1010 (10)
*11 (3)
1010
1010#
11110 (30)

## Slide 5: Representation of Binary Numbers
Binary numbers comprises in two groups.
Unsigned Numbers
Signed Numbers
Unsigned Numbers:- It contains only magnitude of the number .they do not have any sign.
That means all Unsigned binary numbers are positive .
As in decimal number system ,the placing of the +Ve Sign in front of the number is optional.
Example:-(108)10 =(1101100)2 here 7 bits represent the magnitude of number 108.

## Slide 6
Signed Numbers:- It contains both sign and magnitude of the number.
The sign is placed in front of number +Ve sign for positive number and – sign for negative number.
In binary, sign bit is 0 indicates the number is positive and if sign bit is 1 means the number is negative.

## Slide 7: Representation of signed binary numbers
MSB is used to indicate the sign of the number , it is also called sign bit.
If signed binary numbers contains N bits then (N-1) bits only represent the magnitude of numbers.
Three types of representation for signed binary numbers.
Sign- Magnitude form
1’S Complement form
2’S Complement form

## Slide 8: Sign-Magnitude form
Example :- Positive number (108)
Binary equivalent of this number is (1101100) Which contains 7 bits.
Sign binary representation of this number is
(+108)= 0 1101100
(-108)= 1 1101100
Sign bit
Magnitude
Sign bit
Magnitude

## Slide 9: 1’S Complement form
Example :- Negative number (-108)
We know the Signed Binary representation of 108 is (01101100).
Replace all Zero’s by One and all One’s by Zero’s.
01101100
10010011 =(-108) 1’s Complement of (108)10

## Slide 10: 2’S Complement form
The 2’S Complement form of a binary number is obtained by adding one to the 1’S Complement of signed binary number.
Example:-
2’S Complement of (108)=1’S Complement of (108) +1
Binary of 108 = 01101100
1’S Complement of (108) = 10010011
+1
=(10010100)

## Slide 11: Signed Binary Numbers