## Slide 1: PRODUCT OF SUM(POS) & SUM OF PRODUCT(SOP)
BY:
ROSHNI PATOA
COMPUTER SYSTEM ARCHITECTURE

## Slide 2: INTRODUCTION
SOP (Sum of Products) and POS (Product of Sums) are standard forms used in digital logic design.
They are used to simplify Boolean expressions and implement logic circuits.
Both forms are essential for understanding combinational logic systems.

## Slide 3: Sum of Products (SOP)
SOP is a Boolean expression represented as a sum (OR) of product terms.
Each product term is a combination of literals (variables or their complements) connected by AND operations.
Example: F(A, B, C) = A'B'C + AB'C' + ABC.
SOP is derived from truth table rows where the output is 1.

## Slide 4: Implementing SOP
SOP is implemented using:
    AND gates for product terms.
    OR gates to combine the terms.
    Example Circuit:
      F(A, B) = A.B + A’.B'

## Slide 5: Implementing SOP
Steps to Derive SOP
  Identify Rows Where F=1.
  Look at the truth table and note the rows where F=1.
  Here, F=1 for:
  A=0,B=1
  A=1,B=0
  Write the Minterms:
  For each row where F=1, write the corresponding product term (minterm).
  A minterm includes:
    The variable if it is 1.
    The complement (A′ or B′) if it is 0.
  From the truth table:
  For A=0,B=1: A′B
  For A = 1, B = 0: AB′
  Combine the Minterms with OR (Sum):
  Combine the product terms using the OR operator:
  F=A′B+AB′

## Slide 6
Canonical SOP
A specific type of SOP where each product term is a minterm, representing a unique combination of all variables in the function.
Minterms are derived from rows in the truth table where the output is 1.
Example: For a truth table with two variables AA and BB, if FF is true for A=0,B=1 and A=1,B=1:
Canonical SOP: F(A,B)=A′B+AB
Every product term includes all variables.

## Slide 7
STANDARD SOP
A general Boolean expression is represented as the logical OR (sum) of multiple AND (product) terms.
Each product term includes any combination of variables and their complements.
Example: F(A,B)=A′B+AB
Not necessarily canonical because it doesn't require all variables to appear in every product term.

## Slide 8: Product OF Sum (POS)
POS is a Boolean expression represented as a product (AND) of sum terms.
Each sum term is a combination of literals connected by OR operations.
Example: F(A, B, C) = (A + B + C')(A' + B + C)(A + B' + C).
POS is derived from truth table rows where the output is 0.

## Slide 9: Implementing POS
POS is implemented using:
    OR gates for product terms.
    AND gates to combine the terms.
    Example Circuit:
      F(A, B) = (A + B).(A' + B')

## Slide 10: Implementing POS
Steps to Derive POS
  Identify Rows Where F=0.
  Look at the truth table and note the rows where F=0.
  Here, F=0 for:
  A=0,B=0
  A=1,B=1
  Write the Maxterms:
  For each row where F=0, write the corresponding sum term (maxterm).
  A maxterm includes:
    The variable if it is 0.
    The complement (A′ or B′) if it is 1.
  From the truth table:
  For A=0,B=0: (A+B)
  For A = 1, B = 1: (A’+B’)
  Combine the Maxterms with AND (Product):
  Combine the product terms using the AND operator:
  F=(A+B).(A’+B’)

## Slide 11
Canonical POS
A specific type of POS where each sum term is a maxterm, representing a unique combination of all variables in the function.
Maxterms are derived from rows in the truth table where the output is 0.
Example: For a truth table with two variables AA and BB, if FF is false for A=0,B=1, A=1,B=1:
Canonical POS: F(A,B)=(A+B’).(A’+B’)
Every sum term includes all variables.

## Slide 12
STANDARD POS
A general Boolean expression is represented as the logical AND (product) of multiple OR (sum) terms.
Each sum term includes any combination of variables and their complements.
Example: F(A,B)=(A+B’).(A’+B’)
Not necessarily canonical because it doesn't require all variables to appear in every sum term.

## Slide 13
COMPARISON OF SOP & POS
SOP: OR of ANDs, derived from output 1.
POS: AND of ORs, derived from output 0.
SOP is easier for NAND-NAND implementations.
POS is easier for NOR-NOR implementations.
Both forms are used based on design requirements.

## Slide 14
TRUTH TABLE TO SOP & POS
Truth table example:
  Inputs: A, B | Output: F
  Row 1: 0, 0 | 0
  Row 2: 0, 1 | 1
  SOP: F = A'B.
  POS: F = (A + B')(A' + B).

## Slide 15
APPLICATIONS OF SOP & POS
SOP and POS are critical in:
  Digital circuit design.
  Logic minimization.
  Implementation of multiplexers and decoders.

## Slide 16
CONCLUSION
SOP and POS are fundamental concepts in digital logic.
They simplify and optimize the design of logic circuits.
Understanding these forms is essential for advanced digital systems design.
Practice converting truth tables into SOP and POS forms to master the topic.